## Slide 1: Chapter 4: Light and Optics
Beck Peterson

## Slide 2: Light and Optics
Physics
Perception
Hardware

## Slide 3: Light and Optics
Physics
Perception
Hardware

## Slide 4: Physics: How it works
Light
Interactions
Equations

## Slide 5: Physics: How it works
Light
Interactions
Equations

## Slide 6: Light
Waves, Rays, and Photons
Density on light decreases quadratically with distance
Will not converge without a lens

## Slide 7: Light
Absorption, Transmission, and Reflection
Specular (flat) and Diffuse (rough) reflections
Lasers emit coherent (aligned) light
We can inspect non-coherent light using a spectrograph

## Slide 8: Physics: How it works
Light
Interactions
Equations

## Slide 9: Physics: How it works
Light
Interactions
Equations

## Slide 10: Interactions
Lenses and mirrors are thousands of years old
Prisms bend light twice, both entering and exiting
Convex lenses have a focal point where all entered light converges
The focal point for real light will be further than a theoretical Collimated light (infinitely far source)

## Slide 11: Interactions
If an object is closer than the focal distance of a lens, its image will not converge
Concave lenses magnify an image by causing the rays to diverge
Negative focal length can be used to think about the image by doing the calculation in reverse
We can calculate light traveling through multiple lenses by adding lenses diopters. A diopter is the inverse of a lens’ focal length

## Slide 12: Physics: How it works
Light
Interactions
Equations

## Slide 13: Physics: How it works
Light
Interactions
Equations

## Slide 14: Equations
f = s / λ, f ≡ frequency, s ≡ speed, λ ≡ wavelength
Visible light in air is 400-800 terahertz
n = c / s, n ≡ refractive index, c ≡ speed in vacuum, s ≡ speed in medium
n ≈ 1 in air, n ≈ 1.33 in water, n ≈ 1.5 in glass

## Slide 15: Equations
n1sinθ1 = n2sinθ2, θ1 ≡ angle from normal pre-interaction, θ2 ≡ angle from normal post-interaction
Reflects if (n1 / n2)sinθ1 > 1
1 / f - 1 / s1 = 1 / s2, f ≡ theoretical focal length, s1 ≡ distance of light source, s2 ≡ real focal distance
(n2 - n1)(1 / r1 + 1 / r2) = 1 / f, assuming a relatively thin lens, r1 ≡ front radius of lens, r2 ≡ back radius of lens
D = 1 / f, D ≡ diopter, f ≡ focal length

## Slide 16: Physics: How it works
Light
Interactions
Equations

## Slide 17: Light and Optics
Physics
Perception
Hardware

## Slide 18: Light and Optics
Physics
Perception
Hardware

## Slide 19: Perception: How we see it
Colors
The Eye
Imperfections

## Slide 20: Perception: How we see it
Colors
The Eye
Imperfections

## Slide 21: Colors
Rainbow vs pink
Some animals can see Infrared or Ultraviolet
All wavelengths make white, none make black

## Slide 22: Colors
Pigments mix differently than light
Objects appear the colors that they don’t absorb
Red and green light make yellow

## Slide 23: Perception: How we see it
Colors
The Eye
Imperfections

## Slide 24: Perception: How we see it
Colors
The Eye
Imperfections

## Slide 25: The Eye
Four internal mediums: cornea, aqueous fluid, lens, and vitreous fluid with refractive indices between 1.3 and 1.45
Has a total of 60D focusing Collimated light just 17mm from the outer cornea
Irregular eye shape needs to be corrected with complex lenses
Inner ocular chromatic aberrations often occur but are corrected by the brain

## Slide 26: The Eye
The inner lens can be stretched by a muscle to accommodate different focal distances
Babies can accommodate +20D focusing just 5cm from their eyes
Young adults can accommodate +10D
Middle-aged adults can barely accommodate
Low diopters in eyes are called hyperopia or farsightedness
High diopters are called myopia or nearsightedness

## Slide 27: Perception: How we see it
Colors
The Eye
Imperfections

## Slide 28: Perception: How we see it
Colors
The Eye
Imperfections

## Slide 29: Imperfections
Reality is full of imperfections which are hard to replicate
Natural light is a mess of random wavelengths of light
Many imperfections on lenses are called aberrations
Imperfections in lenses can cause different lights to not react equally
Images misaligned with a lens will cause the image to stretch in the direction of the misalignment

## Slide 30: Imperfections
Spherical aberrations cause light to be refracted more further from the center of a lens creating differing focal lengths
Barrel distortions are like fisheye lenses
Pincushion distortions are the opposite
Coma is an aberration of images from far away. It manifests like the trail of a comet
Lens flares occur when there is a very bright light source that causes rings to appear in the image

## Slide 31: Perception: How we see it
Colors
The Eye
Imperfections

## Slide 32: Light and Optics
Physics
Perception
Hardware

## Slide 33: Light and Optics
Physics
Perception
Hardware

## Slide 34: Hardware: How we capture and replicate it
Cameras
Displays

## Slide 35: Hardware: How we capture and replicate it
Cameras
Displays

## Slide 36: Cameras
Can be considered a digital eye
Apertures and shutters affect amount of light
Apertures affect depth of field

## Slide 37: Cameras
Shutters balance motion blur and sensor saturation
CMOS sensors are rolling shutters
CCD shutters are global shutters
Rolling shutters artifact with fast moving subjects

## Slide 38: Hardware: How we capture and replicate it
Cameras
Displays

## Slide 39: Hardware: How we capture and replicate it
Cameras
Displays

## Slide 40: Displays
The book defines a display as a device that stimulates a sense organ
Camera obscura
Cathode ray tubes (scan)
LCD, LED, and OLED (pixel)
VR headsets are too close to focus on, so lenses are used to assist the eye

## Slide 41: Hardware: How we capture and replicate it
Cameras
Displays

## Slide 42: Light and Optics
Physics
Perception
Hardware

## Slide 43: Light and Optics
Physics
Perception
Hardware

## Slide 44: Thank You
Beck Peterson